## Slide 1: Combating Multi-camera Interference using Carrier Sensing
DIVYANSHU SAXENA
ABISHEK KUMAR
https://github.com/MCI/Combating MCI using Carrier Sensing

## Slide 2: Background: 3D Cameras
3D imaging is being used by vision and robotic systems to recover 3D scene geometry - important for technologies such as autonomous transportation, augmented reality, and robot navigation.
Active 3D Cameras - use a programmable light source to emit coded light, which is used for scene depth estimation.
Specifically, cameras that use the Time-of-flight (ToF) principle are proving useful for this purpose.
As these cameras become more ubiquitous, they face the problem of interference.

## Slide 3: Problem Statement: Multi-camera Interference (MCI) in ToF Cameras
The presence of interfering cameras, we face the issue of depth errors - due to phase shifts
https://wisionlab.cs.wisc.edu/project/stochastictdma/

## Slide 4: Motivation: Utilize Wireless Protocols
Interference is a widely studied problem in wireless systems.
In RF Systems, the transmitter sends the data which is carried by the channel to the receiver.
In the MCI scenario, the transmitter sends a light beam, which picks up data from the object and reflects back to the receiver.
Interference happens at the receiver in both cases!

## Slide 5: Prior Work: Different Modulation Frequencies
Most conventional systems using ToF Cameras propose using different modulation frequencies for each camera.
However, while this does reduce the interference in the oscillating part - it fails to eliminate the interference in the constant part of the emitted light.
Leads to lower SNR and hence, does not solve the problem completely!

## Slide 6: Prior Work: Stochastic Exposure Coding
Similar to the Wireless Protocol Slotted Aloha.
Instead of keeping the emitter and sensor ‘on’ at all times, do a probabilistic switch on-off procedure to reduce the chances of collisions.
https://wisionlab.cs.wisc.edu/project/stochastictdma/

## Slide 7: Prior Work: Stochastic Exposure Coding
Similar to the Wireless Protocol Slotted Aloha.
Instead of keeping the emitter and sensor ‘on’ at all times, do a probabilistic switch on-off procedure to reduce the chances of collisions.
There ain’t no free lunch!!!
  Increase in the Total Integration Time
  Decrease in the Effective Exposure Time
The points above lead to the following constraints:
  Increase in Source Power Amplification - to counter the decrease in effective exposure time.
  Choice of the Slot ON probability

## Slide 8: Prior Work: Stochastic Exposure Coding
Similar to the Wireless Protocol Slotted Aloha.
Instead of keeping the emitter and sensor ‘on’ at all times, do a probabilistic switch on-off procedure to reduce the chances of collisions.
Handling Collisions: Post receive mechanism - if the received light intensity in a slot is higher than the “usual”, declare it a clashed slot.

## Slide 9: Intervention: Use Carrier Sensing
Observation:
  The current approach of stochastic slots and then do collision detection, is a passive approach. A more active approach can be used.
  Drawing inspiration from wireless CSMA-CA protocol, we avoid collisions instead of detecting them.
Additional Benefit: We may not suffer from the Hidden Terminal/Exposed Terminal problems in the MCI scenario.
  Occurs widely in wireless systems because transmitter is unaware of the channel state at receiver.
  In MCI, transmitter-receiver are co-located!
Result: We still use multiple slots in the total integration time, but the camera only emits light post sensing the channel.

## Slide 10: Intervention: Algorithm
1 At each slot
2 Sense the channel to see if it is busy
3 If channel is busy
4 Defer the current slot
5 Else
6 Transmit light and receive from the object post reflection
7 Employ collision detection to check if no camera interfered
8 Use the non clashed slots for depth estimation

## Slide 11: Results: Simulation
We evaluate the carrier sensing protocol in an MCI environment, where other cameras may randomly switch on-off with some probability in the entire duration.
Comparison Baselines:
  PN (Pseudonoise): Uses non-sinusoid modulation and demodulation functions. Proposed for early ToF cameras in 2007.
  ACO (AC Orthogonal): Using orthogonal frequencies for the interfering cameras.
  SEC (Stochastic Exposure Coding): Makes use of a stochastic TDMA protocol
  CMB: Combined ACO and SEC
  CSMA: Intervention to use a-priori carrier sensing

## Slide 12: Results: Simulation
Comparison Baselines:
  PN (Pseudonoise): Uses non-sinusoid modulation and demodulation functions.
  ACO (AC Orthogonal): Using orthogonal frequencies for the interfering cameras.
  SEC (Stochastic Exposure Coding): Makes use of a stochastic TDMA protocol
  CMB: Combined ACO and SEC
  CSMA: Intervention to use a-priori carrier sensing
Following results are for CSMA approach using the same Power Amplification as SEC
Inverse Standard Deviation
Interfering Cameras

## Slide 13: Results: Simulation
Comparison Baselines:
  PN (Pseudonoise): Uses non-sinusoid modulation and demodulation functions.
  ACO (AC Orthogonal): Using orthogonal frequencies for the interfering cameras.
  SEC (Stochastic Exposure Coding): Makes use of a stochastic TDMA protocol
  CMB: Combined ACO and SEC
  CSMA: Intervention to use a-priori carrier sensing
Following results are for CSMA approach using the half Power Amplification as SEC
Inverse Standard Deviation
Interfering Cameras

## Slide 14: Results: Simulation
Comparison Baselines:
  PN (Pseudonoise): Uses non-sinusoid modulation and demodulation functions.
  ACO (AC Orthogonal): Using orthogonal frequencies for the interfering cameras.
  SEC (Stochastic Exposure Coding): Makes use of a stochastic TDMA protocol
  CMB: Combined ACO and SEC
  CSMA: Intervention to use a-priori carrier sensing
Following results are for CSMA approach using the half Power Amplification as SEC and 10% increase in probability p_CMB
Inverse Standard Deviation
Interfering Cameras

## Slide 15: Results: Simulation
The average number of ON slots for the camera following the CSMA protocol, in an MCI environment of interfering cameras switching on and off in each slot with a probability:
  Total slots in the integration time = 500

## Slide 16: Next Steps
Evaluate under more circumstances of power amplifications and ON probabilities of interfering cameras.
Simulate a real world setting where each interfering camera can follow a different protocol.
Theoretical bounds for the peak power amplification for the carrier sensing protocol.
Verify feasibility of slot durations in real ToF cameras.